## Slide 1
Solar Power Plant
Generation Forecasting & Anomaly Detection
Data Science Mini-Project · Dataset 4
Member A
Member B
Member C
Member D
Member E
Member F
Notes: Hi everyone — we're [Member A, B, C, D, E, F], and our project is on solar power plant data. We worked on two things: predicting how much power a plant generates based on weather, and automatically catching inverters that are performing worse than they should be. Let's get into it.

## Slide 2
PROBLEM STATEMENT
What Are We Solving?
Regression
Predict AC power output from weather sensor readings
Anomaly Detection
Flag inverters that underperform vs. their expected output
DATA SOURCES
Plant 1 Generation
22 inverters · May–Jun 2020 · 15-min readings
Plant 2 Generation
22 inverters · same period · 15-min readings
Solar Recording
Weather · radiation, temp, humidity, wind
44
days of data
22
inverters / plant
96
readings / day
~135K
total rows
Notes: So the problem has two parts. Regression: given the weather at any moment — radiation, temperature, humidity — can we predict how much power the plant is generating? Anomaly detection: once we know what a plant should be producing, we can flag individual inverters that consistently come in below that. That's actually useful in practice — it tells you which inverters might need maintenance. We had three datasets. Two generation datasets, one per plant, with 15-minute readings from 22 inverters each. And a weather dataset sampled every few minutes.

## Slide 3
EDA · DATA QUALITY
Two Bugs We Caught Before Modelling
Bug #1 · Unit Mismatch
Plant 1 AC/DC ratio = 0.098
Real inverter efficiency is 95–99%
Ratio identical across all 22 inverters
→ DC recorded at 10.2× scale of AC
 | Before | After fix
AC/DC ratio | 0.098 | 0.977
Physically OK? | No ✗ | Yes ✓
Fix: divided Plant 1 DC_POWER by 10.22
Bug #2 · Counter Overflow
Plant 2 TOTAL_YIELD max = 2.24 billion
Plant 1 max = only 7.8 million (same sensor)
Affects 16 of 22 inverters
→ Data logger counter reset / overflow bug
 | Plant 1 | Plant 2
Max TOTAL_YIELD | 7.8 M | 2.24 B ✗
Usable? | Yes ✓ | No ✗
Fix: used DAILY_YIELD instead (unaffected)
Notes: Before we ran any models, we did a quick sanity check on the data — and found two pretty big issues. The first one is in Plant 1. The DC to AC ratio was 0.098. That's physically impossible — a real inverter is 95 to 99% efficient, not 9.8%. What made it obvious it wasn't a hardware fault is that the ratio was identical to five decimal places across all 22 inverters. So it had to be a recording difference. Plant 1's DC power was logged at about 10 times the scale of the AC. We divided it out, and after that both plants showed 97.7% efficiency — completely normal. The second bug is in Plant 2's cumulative yield. Some inverters were showing values in the billions — Plant 1 maxed out at 7.8 million. That's a data logger counter overflow: when the counter hits its limit it wraps back to zero, and the running total goes wrong. Sixteen of 22 inverters were affected. We just dropped that column and used the daily yield instead, which was fine. Catching these before modelling mattered — if we hadn't, our cross-plant comparisons would've been completely off.

## Slide 4
EXPLORATORY DATA ANALYSIS
Patterns We Found in the Data
Radiation is king
Strongest predictor — near-linear relationship with AC output
Bell curve every day
Output peaks 10am–2pm and falls symmetrically — same pattern both plants
Inverter variance
Some inverters consistently yield less than their neighbours under same weather
Heatmap tells the story
Row of red = broken inverter. Column of red = cloudy day affecting everyone.
Notes: For EDA we plotted the standard stuff — daily trends, hourly profiles, scatter plots, boxplots. A few things stood out. Radiation is by far the strongest driver — the scatter plot is almost linear once you remove nighttime readings. Both plants follow the exact same bell curve through the day — peaks around noon, falls off either side. There's also real variation between inverters. Some are consistently producing less than their neighbours under the same weather. You can see it in the boxplot. And the most useful visualisation was the inverter × date heatmap. Each cell is one inverter on one day, coloured by how well it performed relative to its own best. A full row of red means that inverter has a persistent problem. A full column means it was just a bad weather day. That distinction is really important for the anomaly detection step.

## Slide 5
MACHINE LEARNING · REGRESSION
Predicting AC Power from Weather
INPUT FEATURES
Radiation (W/m²) ← most important
Temperature
Humidity
Wind Speed
Hour of Day
Hour from Solar Noon
Month
MODEL COMPARISON (R² on Plant 1 test set)
Chart: 
| Linear Regression | Ridge Regression | Gradient Boosting | Random Forest
R² | 0.72 | 0.73 | 0.91 | 0.95
TimeSeriesSplit CV · RandomizedSearchCV tuning · Cross-plant test (Plant 1 model → Plant 2)
Notes: For regression we tried four models: Linear Regression, Ridge, Gradient Boosting, and Random Forest. Random Forest won — R² of 0.95 on the test set, so it explains 95% of the variation in AC output from weather data alone. One thing we were careful about: we didn't do a random train-test split, because that leaks future data into training. We used TimeSeriesSplit, which keeps splits in time order. We also ran RandomizedSearchCV to tune the Random Forest — things like max depth and number of features at each split. And as a sanity check, we took the model trained on Plant 1 and ran it on Plant 2. It still held up, which tells you the weather-to-power relationship is basically physics — it doesn't depend on which specific plant you trained on.

## Slide 6
ANOMALY DETECTION · ISOLATION FOREST
Flagging Underperforming Inverters
HOW IT WORKS
1
Predict expected AC output per inverter from weather
2
Compute residual = actual − predicted
3
Aggregate: daily performance metrics per inverter
4
Run Isolation Forest on those metrics
5
Rank inverters by anomaly rate → inspection list
RESULTS
~10%
inverter-days flagged
22
inverters ranked
0.977
avg performance ratio (both plants)
Key insight
Persistent red row in heatmap = inverter fault
Full red column = weather event (all inverters affected)
Notes: For anomaly detection, we used Isolation Forest — which we learned outside the course. The idea is straightforward: use the regression model to predict what each inverter should be generating given the weather at that point in time. Then compute the gap between actual and predicted. Aggregate that into daily metrics per inverter — mean residual, performance ratio, standard deviation. Then run Isolation Forest on those numbers to find the outliers. About 10% of inverter-days came back flagged. Some inverters showed up as anomalous day after day — those are your hardware problems, things like soiling, shading, or degraded cells. Others only appeared on specific dates — and when you check, those same dates show all inverters dipping together, meaning it was just bad weather. The heatmap makes this really clear. Full row of red, broken inverter. Full column of red, cloudy day. That's something a plant operator could actually use.

## Slide 7
CONCLUSIONS
What We Found, What We Learned
OUTCOMES
Random Forest → R² = 0.95 on holdout test
Radiation + hour of day dominate predictions
Model generalises across both plants
~10% of inverter-days flagged as anomalous
Caught 2 real data recording bugs pre-modelling
NEW BEYOND COURSE
Isolation Forest (anomaly detection)
TimeSeriesSplit cross-validation
RandomizedSearchCV hyperparameter tuning
SHAP value explainability
merge_asof for time-series joining
Performance ratio KPI (IEC 61724)
Notes: To wrap up — Random Forest gave us R² of 0.95, meaning the weather data alone explains 95% of the variation in power output. The model also transferred to Plant 2 without retraining. For anomaly detection, we ranked all 22 inverters and identified the ones worth inspecting. And before any of that, we caught two real data quality issues — a unit mismatch in Plant 1's DC readings, and a counter overflow in Plant 2's cumulative yield. Both fixed before modelling. For new things beyond the course: Isolation Forest, TimeSeriesSplit, RandomizedSearchCV, SHAP values for explainability, merge_asof for joining time-series at different frequencies, and the performance ratio metric from IEC 61724 — an actual industry standard for solar plant monitoring.

## Slide 8
TEAM
Who Did What
Member A
Data loading, datetime parsing, weather resampling, merge_asof pipeline
Member B
Data quality investigation — unit mismatch detection, counter overflow fix
Member C
EDA — visualisations, heatmaps, correlation analysis, inverter boxplots
Member D
Regression models, TimeSeriesSplit CV, RandomizedSearchCV tuning
Member E
SHAP value explainability, feature importance, cross-plant evaluation
Member F
Anomaly detection pipeline, Isolation Forest, inverter ranking
Thank you · Any questions?
Notes: And here's how we split up the work across the six of us. Member A handled data loading and preprocessing — parsing the two different datetime formats, resampling the weather data to 15-minute intervals, and joining everything together. Member B did the data quality investigation — that's where we found the unit mismatch in Plant 1 and the counter overflow in Plant 2. Member C handled EDA — all the visualisations, heatmaps, boxplots, and correlation analysis. Member D built the regression pipeline — the four models and the time-series cross-validation and tuning. Member E did the SHAP analysis and feature importance, and tested the model on Plant 2. Member F built the anomaly detection — Isolation Forest, inverter ranking, the full pipeline. Thanks for listening.